## Slide 1: Traffic Light Circuit
Group project 3#
CPIT210 | Prof. Md Abdulhamid
7th of December 2021

## Slide 2: Group members:
Albaraa Jamal Bashmmakh | 2035918
Faisal Omar Balamash | 2036827
Abdulaziz Alfozan | 2036008
Abdulrahman Almehdar | 2035596
Mohammed Akif | 2037305

## Slide 3: Content:
Introduction
The integrated circuit used
How the integrated circuits work

## Slide 4: Introduction:
This circuit is used to control traffic a four way traffic light control system, so it makes each traffic light work when it’s needed to be green or yellow and when it’s not.

## Slide 5: Integrated circuits:
74193 IC - Presentable 4-bit binary up/down counter.
74175 IC - Quad D flip-flop
74151 IC – 8-Input Multiplexer
74138 IC – 3-to-8 Decoder
74139 IC – 2-to-4 Decoder

## Slide 6: How the integrated circuits work:
74193 IC - Presentable 4-bit binary up/down counter.
The 74193 is an UP/DOWN MODULO-16 Binary Counter. Separate
Count Up and Count Down Clocks are used and in either counting mode the
circuits operate synchronously. The outputs change state synchronous with
the LOW-to-HIGH transitions on the clock inputs.
Separate Terminal Count Up and Terminal Count Down outputs are
provided which are used as the clocks for a subsequent stages without extra
logic, thus simplifying multistage counter designs. Individual present inputs
allow the circuits to be used as programmable counters. Both the Load and the
Reset (R) inputs asynchronously override the clocks.

## Slide 7: How the integrated circuits work:
74193 IC - Presentable 4-bit binary up/down counter.
State Diagram:
1101
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1110
0001
0000
1101

## Slide 8: How the integrated circuits work:
74193 IC - Presentable 4-bit binary up/down counter.
Transition Table:
Input |  | Current State |  |  |  | Next State |  | 
T0 | TA | Q2 |  | Q1 | Q0 | Q2⁺ | Q1⁺ | Q0⁺
0 | x | 0 |  | 0 | 0 | 0 | 0 | 0
1 | x | 0 | 0 |  | 0 | 0 | 0 | 1
x | 0 | 0 | 0 |  | 1 | 0 | 0 | 1
x | 1 | 0 | 0 |  | 1 | 0 | 1 | 0
0 | x | 0 | 1 |  | 0 | 0 | 1 | 0
1 | x | 0 | 1 |  | 0 | 0 | 1 | 1
x | 0 | 0 | 1 |  | 1 | 0 | 1 | 1
x | 1 | 0 | 1 |  | 1 | 1 | 0 | 0
0 | x | 1 | 0 |  | 0 | 1 | 0 | 0
1 | x | 1 | 0 |  | 0 | 1 | 0 | 1
x | 0 | 1 | 0 |  | 1 | 1 | 0 | 1
x | 1 | 1 | 0 |  | 1 | 1 | 1 | 0
0 | x | 1 | 1 |  | 0 | 1 | 1 | 0
1 | x | 1 | 1 |  | 0 | 1 | 1 | 1
x | 0 | 1 | 1 |  | 1 | 1 | 1 | 1
x | 1 | 1 | 1 |  | 0 | 0 | 0 | 0

## Slide 9: How the integrated circuits work:
74193 IC - Presentable 4-bit binary up/down counter.
State diagram for finite state machine :
Ng
Na
Wg
Wa
Ea
Eg
Sa
Sg
x1
x1
x1
x1
1x
1x
1x
1x
0X
0X
0X
0X
X0
X0
X0
X0

## Slide 10: How the integrated circuits work:
74175 IC - Quad D flip-flop.
The 74175 is a high speed Quad D Flip-Flop. The device is useful for general flip-flop requirements where clock and clear inputs are common. The information on the D inputs is stored during the LOW to HIGH clock transition. Both true and complemented outputs of each flip-flop are provided. A Reset input resets all flip-flops, independent of the Clock or D inputs, when LOW.
Logic symbol

## Slide 11: How the integrated circuits work:
74151 IC – 8-Input Multiplexer.
The 74151 is a high speed 8-input Digital Multiplexer. It provides, in one package, the ability to select one bit of data from up to eight sources. The 74151 can be used as a universal function generator to generate any logic function of four variables. Both assertion and negation outputs are provided.
Logic symbol

## Slide 12: How the integrated circuits work:
74151 IC – 8-Input Multiplexer.
Traffic light control Table :
Current State |  |  | output |  |  |  |  |  |  | 
 |  |  | North |  | West |  | South |  | East | 
Q2 | Q1 | Q0 | B | A | B | A | B | A | B | A
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 13: How the integrated circuits work:
74138 IC – 3-to-8 Decoder.
The 74138 is a high speed 3-of-8 Decoder/Demultiplexer. This device is ideally suited for high speed bipolar memory chip select address decoding. The multiple input enables allow parallel expansion to a 1-of-24 decoder using just three 74138 devices or to a 1-of-32 decoder using four 74138 and one inverter.
Logic symbol

## Slide 14: How the integrated circuits work:
74139 IC – 2-to-4 Decoder.
The 74139 is a high speed 2-of-4 Decoder/Demultiplexer. The device has two independent decoders, each accepting two inputs and providing four mutually exclusive active LOW Outputs. Each decoder has an active LOW Enable input which can be used as a data input for a 4-output demultiplexer. Each half of the 74139 can be used as a function generator providing all four minterms of two variables.
Logic symbol

## Slide 15: Thank you